## Slide 1: Building the Internet of Things…
With JavaScript???

## Slide 2: Hi. I’m Adam
ABOUT ME
Adam Barney
Lincoln, NE
Barney Consulting
Microsoft MVP (C#)
Microsoft ASPInsider
Nebraska.Code()
Lincoln .NET Users Group
@cabarney
adam@adambarney.com
I AM NOT
A JavaScript guy
A hardware guy
A node.js guy
So why am I here???

## Slide 3
Tessel is a microcontroller that runs JavaScript. It's Node-compatible and ships with Wifi built in. Use it to easily make physical devices that connect to the web.

## Slide 4
TI CC3000 WiFi radio built in
180MHz ARM Cortex M3 Microprocessor
32MB/ea RAM and Flash Memory
Micro USB or Batter Power
Programmable via JavaScript
Compatible with 10,000’s of node.js packages through npm
Deploy over USB or remotely by WiFi

## Slide 5
Installing
Updating
Getting online
npm install tessel -g
tessel update
tessel wifi –n <ssid> -p <pw>

## Slide 6
Blinking Lights
tessel run blink.js
var tessel = require('tessel');
setInterval(function() {
tessel.led[0].toggle();
}, 100);

## Slide 8
npm install camera-vc0706
camera.takePicture(function(){});

## Slide 9
Accelerometer
Ambient
Audio
Bluetooth
Camera
Climate
GPS
Infrared
MicroSD Card
nRF24
Relay
Servo

## Slide 10
GPRS
(2G + Phone/SIM)
RFID
+10 community-contributed modules (and counting)

## Slide 11
Thermometer
Proximity
Motion
Liquid Flow
Cameras
Coin slots
Force
Moisture
Wind speed
Keypad
Touch
LCD Screens
NeoPixels
LED Panels
Fluid flow valves
Motors
Lasers
Speakers
Solenoids
Door locks
So many more…
So what can we do?

## Slide 12
RFID
Audio
Relay

## Slide 13
Relay

## Slide 14
Servo

## Slide 15
GPRS
(2G + Phone/SIM)
Audio
MicroSD Card

## Slide 16
Climate
GPS

## Slide 17
GPS
Accelerometer
Camera

## Slide 18
Relay

## Slide 19
Ports
Pins
var portA = tessel.port['A'];
var gpio = tessel.port['GPIO'];
var rfid = lib.use(tessel.port['A']);
var pin = gpio.pin[‘G4'];
var pin = gpio.pwm[0];
var pin = gpio.analog[0];
var pin = gpio.digital[0];
pin.write(1); // output(1)
var val = pin.read();

## Slide 20: DEMOS

## Slide 21: Questions?
tessel.io
adam@adambarney.com
10% Discount code (in case you didn’t get the text): “TESSEL-CODEMASH”