## Slide 1: Building the Internet of Things…
With JavaScript???

## Slide 2: Hi. I’m Adam
ABOUT ME
Adam Barney
Lincoln, NE
Barney Consulting
Microsoft MVP (C#)
Microsoft ASPInsider
Nebraska.Code()
Lincoln .NET Users Group
@cabarney
adam@adambarney.com
I AM NOT
A JavaScript guy
A node.js guy
A hardware guy
So why am I here???

## Slide 3
Tessel is a microcontroller that runs JavaScript. It's Node-compatible and ships with Wifi built in. Use it to easily make physical devices that connect to the web.

## Slide 4
TI CC3000 WiFi radio built in
180MHz ARM Cortex M3 Microprocessor
32MB/ea RAM and Flash Memory
Micro USB or Batter Power
Programmable via JavaScript
Compatible with 10,000’s of node.js packages through npm
Deploy over USB or remotely by WiFi

## Slide 5
Installing
Updating
Getting online
npm install tessel -g
tessel update
tessel wifi –n <ssid> -p <pw>

## Slide 6
Blinking Lights
tessel run blink.js
var tessel = require('tessel');
setInterval(function() {
tessel.led[0].toggle();
}, 100);

## Slide 8
npm install camera-vc0706
camera.takePicture(function(){});

## Slide 9
Accelerometer
Ambient
Audio
Bluetooth
Camera
Climate
GPS
Infrared
MicroSD Card
nRF24
Relay
Servo

## Slide 10
GPRS
(2G + Phone/SIM)
RFID
+10 community-contributed modules (and counting)

## Slide 11
Ports
Pins
var portA = tessel.port['A'];
var gpio = tessel.port['GPIO'];
var rfid = lib.use(tessel.port['A']);
var pin = gpio.pin[‘G4'];
var pin = gpio.pwm[0];
var pin = gpio.analog[0];
var pin = gpio.digital[0];
pin.write(1); // output(1)
var val = pin.read();

## Slide 12
Thermometer
Proximity
Motion
Liquid Flow
Cameras
Coin slots
Force
Moisture
Wind speed
Keypad
Touch
LCD Screens
NeoPixels
LED Panels
Fluid flow valves
Motors
Lasers
Speakers
Solenoids
Door locks
So many more…
So what can we do?

## Slide 13
RFID
Audio
Relay
Notes: Door access / alarm

## Slide 14
Relay
Notes: Motion activated lights (turn off the bathroom lights when you’re done!)

## Slide 15
Servo
Notes: BBQ temperature regulator

## Slide 16
GPRS
(2G + Phone/SIM)
Audio
MicroSD Card
Notes: A Phone!!! (with MP3 player)

## Slide 17
Climate
GPS
Notes: Automated moisture-sensing watering system

## Slide 18
GPS
Accelerometer
Camera
Notes: Fleet tracking (add relay for teenage driver embarrassment)

## Slide 19
Relay
Notes: Turn on/off power based on wind speed (inflatable Christmas yard decorations)

## Slide 20: DEMOS

## Slide 21: Questions?
tessel.io
adam@adambarney.com
10% Discount code (in case you didn’t get the text): “TESSEL-CODEMASH”